## Slide 1
SLIDE 17
High-Level Architecture
1. Frontend Tier
HTML5 / CSS / Vanilla JS Chart.js • WebSocket Client REST Fetch API
2. Backend Tier
FastAPI (async Python) Routers • AI Engine • Security Engine SQLite DB • WebSocket Manager
3. Hardware Tier
Raspberry Pi 5 (4GB) Built-in Wi-Fi & BLE USB Dongles: Zigbee / Thread / Z-Wave RC522 / PN532 RFID Reader
➔
➔
Frontend ── HTTP REST + WebSocket ── Backend ── SQLAlchemy ORM ── SQLite ── Nmap / Bleak ── Hardware

## Slide 2
SLIDE 18
Hardware Architecture
🍓 Central Unit
Raspberry Pi 5 — 4 GB RAM Quad-core ARM Cortex-A76 Runs FastAPI + AI Engine + Docker OS: Raspberry Pi OS (64-bit)
⚡ Power Supply
5V / 5A USB-C — stable voltage for all dongles
📡 Zigbee
Sonoff CC2652P USB Dongle Plus Zigbee 3.0 — Mesh network auditing
🧵 Thread/Matter
Nordic nRF52840 Dongle IPv6 smart-home protocol support
🏠 Z-Wave
Aeotec Z-Stick 7 (Z-Wave Plus) Legacy residential automation
📶 LoRaWAN
Dragino USB LoRa Adapter Long-range enterprise networks
🔐 RFID/NFC
RC522 / PN532 SPI-I2C MIFARE Classic & NFC auditing

## Slide 3
SLIDE 19
Software Architecture — Backend
FastAPI Application (async Python)
main.py — App Entry Point CORS • DB Init • Router Mount • /ws endpoint
websocket_manager.py
Global broadcast server Real-time push to all clients
ai_engine.py + security_engine.py
Heuristic analysis • risk scoring Remediation database
database.py (SQLAlchemy + SQLite)
ORM models: Device, Vulnerability, RFIDCard, RFIDScanReport, Setting
Modular Router Architecture (routers/)
iot.py
Network discovery • multi-protocol scans (Wi-Fi, Zigbee, Thread, Z-Wave, LoRaWAN)
wifi_bt.py
Wi-Fi deep port scan • credential attacks BLE audit • deauth module
access_control.py
RFID reader control • attack simulation
ai.py
AI heuristics API • risk scoring endpoints
reports.py
PDF audit report generation (ReportLab)
virtual_lab.py / attack_scenarios.py
Docker lab orchestration • training workflows

## Slide 4
SLIDE 20
Database Design (ERD)
devices
id (PK)
ip UNIQUE
mac
hostname
vendor
protocol
os_guess
risk_level
risk_score
open_ports
last_seen
vulnerabilities
id (PK)
device_id (FK → devices)
vuln_type
severity
description
port
protocol
rfid_cards
id (PK)
uid UNIQUE
card_type
encryption_type
auth_mode
replay_protection
tag_integrity
risk_level
risk_score
last_seen
rfid_scan_reports
id (PK)
uid
attack_type
attack_result
remediation
simulation_status
timestamp
settings
key (PK)
value
1
∞
SQLite — serverless, zero-config, optimized for read-heavy flash storage on Raspberry Pi microSD

## Slide 5
SLIDE 21
AI Engine Design
1
Feature Extraction
Ports • vendor protocol • hostname
→
2
Signature Matching
VULNERABILITY_PATTERNS Camera / Router / PLC / Medical
→
3
Vulnerability Prediction
OPEN_TELNET → port 23 ZIGBEE_DEFAULT_KEY → Zigbee
→
4
Anomaly Detection
Unusual ports Unknown vendor fingerprint
→
5
Risk Score (0–100)
Weighted: ports + CVEs + credentials + TLS
→
6
Remediation Mapping
Step-by-step fix from REMEDIATION_DATABASE
→
7
Dynamic Narrative
AI summary string with confidence %
No TensorFlow / PyTorch — runs entirely on Raspberry Pi CPU using statistical heuristics & rule databases

## Slide 6
SLIDE 22
API Design
REST Endpoints
Method
Path
Purpose
GET
/networks/discover
List active network interfaces
POST
/scan/wifi
Launch Nmap Wi-Fi discovery
POST
/scan/zigbee
Scan Zigbee coordinator nodes
POST
/scan/bluetooth
Run Bleak BLE discovery
GET
/devices
Retrieve all discovered hosts
GET
/analyze/device/{id}
AI deep analysis & remediations
POST
/attack/simulate
Trigger access control simulation
GET
/generate/pdf
Compile PDF audit report
WebSocket /ws
heartbeat
Keep-alive ping every 10 s
settings_updated
Broadcast config changes to all clients
scan_update
Live Nmap/Bleak terminal stream

## Slide 7
SLIDE 23
Sequence Diagram — Full Scan Workflow
Security Analyst
Web Frontend
FastAPI Backend
Scan Engine
AI Engine ai_engine.py
SQLite pentex.db
Click "Start Scan"
POST /scan/wifi
Start Nmap thread
Insert discovered devices
WebSocket: "scan_update"
analyze_device(data)
Return risk score + remediations
Update device scores
GET /generate/pdf
Fetch audit statistics
Return PDF download stream